Recent Developments of the fastNLO Toolkit
Daniel Britzger, Klaus Rabbertz, Georg Sieber, Fred Stober, Markus Wobisch

---
Motivation
- Calculation of hadron-hadron collisions at higher orders of perturbative QCD require large amounts of processing power
- Calculations are repeated many times for different parameters.
  - Multiple PDF sets (CT, MSTW, NNPDF, …)
  - Single PDF set: PDF uncertainties
  - Scale uncertainties
  - Used in fitting procedures
- The fastNLO framework allows to quickly evaluate the cross section for different PDFs, values of as and scale choices

---
Introduction
f2(x2)
- Cross section in hadron-hadron collisions in pQCD
- Perturbative coefficients are independent from PDF and αs
- Factorize PDF, αs and scale dependence
- Interpolation
  - Single PDF is decomposed into interpolation kernels
  - Similar interpolation procedure also used for scales
- Convolution integrals become discrete sums
  - Values of perturbative coefficients can be
    stored in a table
  - Interpolation nodes in x and scales are stored
    together in look-up table
size 12{σ= Sum cSub { size 8{a,b,n} } { Int cSub { size 8{0} } cSup { size 8{1} } { ital "dx" rSub { size 8{1} } } Int cSub { size 8{0} } cSup { size 8{1} } { ital "dx" rSub { size 8{2} } α rSub { size 8{s} } rSup { size 8{n} } \( μ rSub { size 8{r} } \) } } cdot c rSub { size 8{a,b,n} } \( x rSub { size 8{1} } ,x rSub { size 8{2} } ,μ rSub { size 8{r} } ,μ rSub { size 8{f} } \) cdot f rSub { size 8{1,a} } \( x rSub { size 8{1} } ,μ rSub { size 8{f} } \) f rSub { size 8{2,b} } \( x rSub { size 8{2} } ,μ rSub { size 8{f} } \) } {}
c
ˆ
f1(x1)

---
Scale variations for NLO
- Renormalization scale variations at NLO
  - Standard method:
    RGE → LO matrix element times nb0ln(cr)
  - Flexible-scale:
    using scale-independent weights
    w(mR,mF) = w0 + log(mR) wR + log(mF) wF
- Factorization scale variations at NLO
  - Store coefficient for given set of
    scale factors
  - Flexible-scale
  - Calculate LO DGLAP splitting functions
    with HOPPET
Scale factor
Cross section [pb/GeV]

---
Scale variations for NNLO
- In General: NLO splitting functions are needed for
  factorization scale variations → slow
- Flexible scale: analogous to NLO + NNLO terms
  using scale-independent weights → additional weights
  w(mR,mF)	=	w0 + log(mR) wR + log(mF) wF
  + log2(mR2) wRR + log2(mF2) wFF + log(mR2) log(mF2) wRF
- Advantages
  - Vary mR, mF independently and by any factor
  - NLO splitting functions are not needed
- fastNLO implementation:
  - Two different observables can be used for the scales
  - Any function of these two observables can be used
    for calculating scales

---
fastNLO Toolkit
Easy integration into NLO / NNLO Programs
- fastNLOCreate fnlo(“steering.str“);
  fnlo.SetOrderOfCalculation(int order)
  fnlo.fEvent.SetProcessID(int id);
  fnlo.fEvent.SetWeight(double w);
  fnlo.fEvent.SetX1(double x1);
  fnlo.fEvent.SetX2(double x2);
  fnlo.fScenario.SetObservable0(double pt);
  fnlo.fScenario.SetObsScale1(double s1);
  fnlo.Fill();
- fnlo.SetNumberOfEvents(double nevents);
  fnlo.WriteTable();
Init
Monte-Carlo
Event loop
End

---
Analysis Workflow
Tomorrow in WG4: Fast evaluation of theoretical
uncertainties with Sherpa and Mcgrid → E. Bothmann
Table
Generation
NLO / NNLO Monte Carlo
Event Generator
Event Analysis
fastNLO
table
fastNLO
toolkit
Sherpa
Rivet
+
MCgrid
NJet
Blackhat
...
fastNLO
toolkit
fastNLO
Native
Analysis
nloJet++
DiffTop
User
Analysis
...
...
...

---
Reading tables
- Access Tables with
  Python or C++
- Generate yoda output
  with fnlo-tk-yodaout
  (with contributions by Stefanos Tyros)
  Foreseen to be used in MCplots.
- LHAPDF 5 / 6
- Different as Evolution codes available
- from fastnlo import fastNLOLHAPDF
- import numpy
- fnlo = fastNLOLHAPDF('fnlotable.tab')
  fnlo.SetLHAPDFFilename('CT10nlo.LHgrid')
  fnlo.SetLHAPDFMember(0)
  mufs = np.arange(0.1, 1.5, 0.10)
  murs = np.arange(0.1, 1.5, 0.10)
  xs = np.zeros((mufs.size, murs.size))
  for i, muf in enumerate(mufs):
  for j, mur in enumerate(murs):
  fnlo.SetScaleFactorsMuRMuF(mur, muf)
  fnlo.CalcCrossSection()
  xs[i][j] = np.array(fnlo.GetCrossSection())[0]

---
Example – DiffTop analysis:
NNLO Accuracy with fastNLO
- Differential ttbar in approx.
  NNLO: dσ/dpT , dσ/dy
- Uncertainties:
  - PDF, scale, αs, mt
    786 variations needed
- Precision study of
  fastNLO tables over
  standalone DiffTop
  vs. no. of x nodes
- Perfect agreement for probed x-range
  of 2 ·10-3 < x < 1

---
Precision measurement of αS(MZ):
Three-Jet Mass Cross Section - Interpolation
- fastNLO allows to use user defined αS evolution codes during the evaluation of the coefficient tables
- Not limited to the αS values supplied by the PDF set anymore
  - This enables the use of proper minimizer libraries like Minuit2 when fitting αS
- Two common :
  - Interpolation:
    - Interpolate between
      two adjacent αS points
  - Extrapolation:
    - Some observables with
      large scale uncertainties
      can reach the edge of
      the αS series of the PDF.

---
Precision measurement of αS(MZ):
Three-Jet Mass Cross Section - Interpolation
- For simple cases, there is good agreement between the interpolation method and the classical parameterization method
- For more complicated situations, in particular with very asymmetric PDF uncertainties, the interpolation method avoids all parameterization related issues

---
New public release
- fastNLO toolkit
  - Support for MCgrid (> v1.2) and Sherpa (including all NLO processes available via this chain)
  - fnlo-tk-yodaout (with contributions by Stefanos Tyros) for YODA-formatted output
  - Triple differential observable Binnings are supported
  - Convenience functions to derive scale uncertainties
  - fnlo-tk-config executable is provided for easier compiling/linking
  - Doxygen documentation
- fastNLO interface to NLOJet++
  - Updated to work with new toolkit prerelease
  - Major simplification in NLOJet++ usage – many use cases possible without code changes
    - InclusiveNJets - one entry per jet of an event
    - InlusiveNJetsEvent - one entry per event.
  - Steering files to reproduce calculations for numerous published cross sections
- fastNLO reader (compatibility update)
  - Adapted to new fastNLO_toolkit
  - Up to 3-dimensional binnings are supported
  - 7 subprocesses for LO hh->jets as used in toolkit is supported
  - Internally used cross section units are rescaled to published units

---
Summary and Outlook
- New public release of the fastNLO toolkit this week
- Toolkit provides all necessary functions to create and evaluate fast interpolation tables in the fastNLO format
- Number of interfaced NLO / NNLO theory programs steadily increasing (via MCgrid or direct interface)
- Fast and accurate evaluation of NLO / NNLO calculations with flexible scales / different as evolutions open up new possibilities for analysis
- Large scale production effort underway to produce
  tables for published results – will be available on
  fastnlo.hepforge.org